The RGB Image files:

These files are R-G-B color separations of a Mercator Projection
of global color shaded relief. No display software is provided on
this CD-ROM, unless your system has enough memory to ingest a
15-megabyte file for each primary color. The files are in 8-bit
pixel raster format, arranged as described below.

There are three Mercator Image files of Red, Green, and Blue 
separates. There is also a color scale bar (2000 pix wide x 131 
lines) with breaks indicated at 9000, 7000, 5000, 3000, 1500, 500, 
200 meters below sea level, and 0, 200, 500, 1000, 2000, 3500, and 
5000 meters above sea level. The endpoints of the scale are at 
11000 meters below and 9000 meters above sea level.

The image files are in the Mercator Projection on a sphere, 
spanning ±80¡ latitude, and from 90¡E around the world plus 90¡ to 
120¡E. There are 3352 lines, each 4682 pixels long, in the image, 
including a blank line (all white) at the top of the image. (There 
is a white pixel at the beginning and end of each line.) There are 
also dotted lines every 10¡ of latitude and longitude. To find a 
specific latitude on the image, count lines away from the center, 
using to the following FORTRAN code to compute a lookup table.

How to find the correct scan line for a given latitude in the 
Mercator Images:

    subroutine mparts(phid)
c ** Compute meridional parts for pixels 5'x5' at equator
c   y = R*alog(tan(pi/4 + phi/2.))
c   phi = pi/2. - 2*atan(exp(-y/R))
c   At Equator, pixel width for 5' is 2*pi/(360*12)
    dimension phid(1676)
    data pi /3.141592654/
    pi2 = pi/2.0
    y5 = 2.*pi/(360.*12.)
c ** Compute latitude "phi" for the 1676 equal y-steps from 
Equator to 80¡
    do 10 i=1,1676
    y = y5*i
c **  This is the inverse Mercator conversion
    phi = pi2 - 2.0*atan(exp(-y))
  10    phid(i) = phi*57.295779
    end

The latitude offsets are symmetrical about the Equator (Line 
1676), so the lookup table need not be repeated for negative 
(south) latitudes. Note that the latitude of a given raster line 
will almost never fall on a whole degree -- the nearest neighbor 
must be used. The computed latitudes ÒphidÓ are in degrees.

If you have any further questions, please call Peter Sloss at 
303-497-6119, or write

Dr. Peter W. Sloss
NOAA/NGDC
Code E/GC3
325 Broadway
Boulder, CO 80303-3328

pws@mail.ngdc.noaa.gov